## Slide 1
WiFi Sniffer
Web Control Panel v4
User Guide
Web-based WiFi packet capture tool for OpenWrt routers
Supports 2.4G / 5G / 6G tri-band capture in Monitor Mode
NETGEAR Confidential

## Slide 2
Overview
Tri-Band Capture
Capture WiFi packets on 2.4G, 5G, and 6G bands simultaneously using tcpdump in Monitor Mode
Web-Based GUI
Browser-based control panel - no additional software needed. Runs on any PC with Python + SSH
OpenWrt Router
Connects to router via SSH. Manages channel config, starts/stops capture, downloads pcap files
Key Features
No paramiko - uses native OpenSSH only
Persistent config (channel, file-split, capture info)
Real-time file size monitoring during capture
Custom pcap filenames with Product Name + SW Version
Input validation on all API endpoints
Architecture
Windows PC
Python + Flask
SSH
OpenWrt Router
tcpdump + iwconfig
Browser (localhost:5000)
NETGEAR Confidential

## Slide 3
Prerequisites
Software Requirements
Python 3.8+
Install from python.org
OpenSSH Client
Windows Settings > Apps > Optional Features
Flask + Flask-SocketIO
pip install -r requirements_v4.txt
Web Browser
Chrome / Edge / Firefox recommended
Network Setup
OpenWrt Router
Router with SSH access enabled
SSH Key Auth
ssh root@192.168.1.1 (passwordless)
Monitor Mode
Router interfaces in Monitor Mode
Network Access
PC and router on same network
NETGEAR Confidential

## Slide 4
GUI Layout Overview
WiFi Sniffer Web Control Panel v4.0
SSH Connected: root@192.168.1.1
Channel Configuration
2.4G: CH 6 | HT40
5G: CH 36 | EHT160
6G: CH 37 | EHT320
Apply Config
File Split: 100 MB | Capture Info: Product Name [ RAX50 ] SW Version [ V1.0.3.120 ] [Save]
Start 2G
Start 5G
Start 6G
Start All
Capture Status
2.4G: Capturing... Duration: 00:02:35 File Size: 12.4 MB
5G: Idle
6G: Idle
A SSH Connection Status
Shows if router is reachable
B Channel Configuration
Set band, channel, bandwidth
then click Apply Config
C Capture Info
Set Product Name + SW Version
for pcap filename prefix
D Capture Controls
Start / Stop per band or all
Buttons change color by state
E Live Status Panel
Real-time duration, file size
updates every 3 seconds
NETGEAR Confidential

## Slide 5
Step 1: Launch the Server
1
1
Double-click start_server_v4.bat
This batch file checks Python, SSH, and dependencies automatically.
2
Wait for server startup
Console will show: "Server running at http://127.0.0.1:5000"
3
Browser opens automatically
If not, manually navigate to http://127.0.0.1:5000
4
Verify SSH connection
Green status bar = connected. Red = check network/SSH setup.
Command Prompt
============================================
WiFi Sniffer Web Control Panel v4.0
============================================
URL : http://127.0.0.1:5000
Debug : False
SocketIO: True
Host : 0.0.0.0
--------------------------------------------
[INFO] SSH pre-check: OK
[INFO] Server started successfully
[INFO] Polling mode active (3s interval)
NETGEAR Confidential

## Slide 6
Step 2: Configure WiFi Channels
2
Channel Configuration
Band
Channels
Bandwidth Options
Method
2.4G
1-14
HT20, HT40
iwconfig
5G
36-165
HT20/40, VHT80, EHT160
iwconfig
6G
1-233
EHT80/160/320
cfg80211tool
How to Configure:
1. Select band dropdown (2.4G / 5G / 6G)
2. Choose channel from the dropdown list
3. Select bandwidth (HT20, VHT80, EHT160, etc.)
4. Click "Apply Config & Restart WiFi"
5. Wait for verification (green = success)
Important Notes
Channel Verification
System reads back actual channel from router to confirm. Uses iwconfig frequency parsing for 2G/5G, cfg80211tool for 6G.
6G Limitations
Not all 6G channels work on every hardware. Channels 65-221 are supported. Channels 1-61 and 225-233 may return error -22.
Apply Kills Captures
Applying config stops all running tcpdump processes. Stop captures first if needed.
Config Persistence
Settings are saved to ~/.wifi_sniffer/config.json and restored on next launch.
NETGEAR Confidential

## Slide 7
Step 3: Set Capture Info (Product & SW Version)
3
Capture Info
Product Name
RAX50
Software Version
V1.0.3.120
Save
Capture info saved successfully
How Capture Info Affects Filenames
Pcap Filename Format:
RAX50
Product
_
V1.0.3.120
SW Ver
_
5G
Band
_
sniffer
Type
_
20260405
Date
_
143022
Time
.pcap
Ext
Examples:
With info: RAX50_V1.0.3.120_5G_sniffer_20260405_143022.pcap
Without info: 5G_sniffer_20260405_143022.pcap
Rules:
Max 30 characters per field
Allowed: a-z, A-Z, 0-9, . _ -
Both fields are optional
Saved persistently to config
NETGEAR Confidential

## Slide 8
Step 4: Start & Monitor Capture
4
Capture Control Buttons
Start 2G
Ready to capture
Stop 2G
Capture running
Start All
Start all 3 bands
Stop All
Stop all bands
Live Status Panel
Band Status Duration File Size File Count
-------------------------------------------------------
2.4G Capturing 00:05:12 24.3 MB 1
5G Capturing 00:05:12 48.7 MB 1
6G Idle --:--:-- -- 0
How It Works
SSH Command
Sends tcpdump command to router via SSH. Captures in Monitor Mode on the selected interface.
Real-Time Updates
Status panel polls every 3 seconds. Shows duration, file size, and file count for each band.
File Split
When file size exceeds the split threshold (default 100MB), a new capture file is started automatically.
Background Process
tcpdump runs in background on router. You can start multiple bands and they run in parallel.
NETGEAR Confidential

## Slide 9
Step 5: Stop Capture & Download Files
5
Stop Workflow
1
Click Stop button
Click "Stop 2G/5G/6G" or "Stop All" to end capture
2
tcpdump terminated
SSH sends kill signal to tcpdump process on router
3
Files downloaded via SCP
Pcap files are copied from router to local PC
4
Files saved locally
Files appear in the download folder with the naming convention
Download Location:
Same folder as wifi_sniffer_web_control_v4.py (project root)
Downloaded Files
Project Folder/
RAX50_V1.0.3.120_2G_sniffer_20260405_143022.pcap
RAX50_V1.0.3.120_5G_sniffer_20260405_143022.pcap
RAX50_V1.0.3.120_6G_sniffer_20260405_143022.pcap
Open with Wireshark for analysis:
> wireshark RAX50_V1.0.3.120_5G_*.pcap
Easily identify captures by:
Product -> RAX50
Firmware -> V1.0.3.120
Band -> 2G / 5G / 6G
Time -> 20260405_143022
NETGEAR Confidential

## Slide 10
Quick Reference: Complete Workflow
1
Launch
Run .bat file
Open browser
2
Configure
Set channel
Set bandwidth
3
Capture Info
Product name
SW version
4
Capture
Start bands
Monitor live
5
Download
Stop capture
Get .pcap files
Tips for Best Results
Always set Capture Info before starting capture - it cannot be changed mid-capture
Use Ctrl+F5 in browser if GUI changes are not visible after server restart
6G channels 65-221 are confirmed working. Other channels may fail depending on hardware
File split at 100MB helps keep pcap files manageable for Wireshark analysis
Status updates every 3 seconds - check Duration and File Size to confirm capture is active
NETGEAR Confidential

## Slide 11
Troubleshooting
SSH Connection Failed (red status bar)
Check: router IP correct? SSH key installed? Run: ssh root@192.168.1.1 manually to test.
GUI not showing new features / layout broken
Press Ctrl+F5 in browser to force reload. Browser may have cached old CSS/JS files.
Apply Config shows FAIL
Channel verification uses frequency parsing. Some channels may not apply due to DFS or hardware limits. Check console log for details.
Duration / File Size not updating
Polling runs every 3 seconds. If still frozen, check WebSocket and polling status in browser console (F12).
6G channel returns error -22
Not all 6G channels work on all hardware. Channels 65-221 are confirmed. Channels 1-61, 225-233 may fail.
Pcap files not downloading after Stop
Check SCP connectivity. Files are on router at /tmp/. Manual download: scp root@192.168.1.1:/tmp/*.pcap .
NETGEAR Confidential

## Slide 12
Thank You
WiFi Sniffer Web Control Panel v4
For questions or issues, contact the QA team
NETGEAR Confidential