## Slide 1
WiFi Sniffer Control Panel v4
Tutorial & Operation Guide
OpenWrt Monitor Mode Packet Capture System
2.4 GHz
5 GHz
6 GHz
NETGEAR | April 2026

## Slide 2
What You'll Learn
01
System Requirements & Setup
What you need before getting started
02
Installation & First Launch
Install dependencies and start the application
03
SSH Connection Setup
Configure SSH access to OpenWrt router
04
Interface & Channel Configuration
Set up WiFi bands, channels, and bandwidth
05
Capture Workflow
Start, monitor, and stop packet captures
06
Product Info & File Naming
Tag captures with product name and SW version
07
Troubleshooting
Common issues and solutions

## Slide 3
System Architecture
Windows PC
WiFi Sniffer v4 (Flask App)
Web Browser (localhost:5000)
SSH Client (OpenSSH)
Downloads Folder
SSH
OpenWrt Router (192.168.1.1)
tcpdump (Monitor Mode)
ath0 - 2.4 GHz Band
ath2 - 5 GHz Band
ath1 - 6 GHz Band

## Slide 4
01 System Requirements
Windows PC
Windows 10/11 (64-bit)
Python 3.8+ installed
OpenSSH Client enabled
Network connection to router
Packages: flask, flask-socketio
OpenWrt Router
OpenWrt firmware
SSH/Dropbear enabled
tcpdump installed
IP: 192.168.1.1 (default)
Monitor mode capable WiFi

## Slide 5
02 Installation & First Launch
1
Clone / Copy Project
Copy wifi_sniffer_v4/ folder to your PC
2
Install Dependencies
pip install flask flask-socketio eventlet
3
Verify SSH
ssh root@192.168.1.1 (must connect without prompt)
4
Launch Application
python run_v4.py or run v4.exe
5
Open Browser
Go to http://127.0.0.1:5000

## Slide 6
03 SSH Connection Setup
SSH Key-Based Authentication (Recommended)
Step 1: ssh-keygen -t ed25519 # Generate key pair
Step 2: type %USERPROFILE%\.ssh\id_ed25519.pub | ssh root@192.168.1.1 "cat >> /etc/dropbear/authorized_keys"
Step 3: ssh root@192.168.1.1 # Verify no password prompt
Verification Checklist
OpenSSH is available: where ssh returns a path
Key-based login works: ssh root@192.168.1.1 connects without password
Router has tcpdump: ssh root@192.168.1.1 which tcpdump returns /usr/sbin/tcpdump

## Slide 7
04 Interface & Channel Configuration
Default Interface Mapping
Band | Interface | Channels | Bandwidths
2.4 GHz | ath0 | 1 - 14 | HT20, HT40
5 GHz | ath2 | 36 - 165 | EHT20 - EHT160
6 GHz | ath1 | 1 - 233 | EHT20 - EHT320
How to Configure
1
Select Channel and Bandwidth for each band from the dropdowns
2
Click "Apply" next to each band to stage the configuration
3
Click "Apply Config & Restart WiFi" to commit all changes to the router
4
Wait for WiFi restart to complete (the modal will show progress)

## Slide 8
05 Capture Workflow
START
Begin Capture
MONITOR
Real-time Status
STOP
End Capture
DOWNLOAD
Save .pcap Files
Single Band:
Click "Start" on any band card (2.4G / 5G / 6G) to begin capture on that band
All Bands:
Click "Start All Captures" to capture on all three bands simultaneously
Monitor:
Real-time file size and duration update every 5 seconds via WebSocket or polling
Stop Single:
Click "Stop & Save" on a band card to stop that band and download the .pcap file
Stop All:
Click "Stop All & Download" to stop all bands and download all .pcap files at once

## Slide 9
06 Product Info & File Naming
NEW
Capture Info Fields
The Capture Info section lets you tag your captures with a Product Name and Software Version. These values are included in the downloaded .pcap filename for easy identification.
Filename Format Examples
Product + SW Version filled
RAX50_V1.0.3.120_5G_sniffer_20260405_143022.pcap
Product Name only
WAX620_2G_sniffer_20260405_143022.pcap
SW Version only
FW2.1_6G_sniffer_20260405_143022.pcap
Both fields empty (backward compatible)
5G_sniffer_20260405_143022.pcap
Values are auto-saved to config.json and restored on next launch. Allowed characters: A-Z, a-z, 0-9, dot, underscore, hyphen (max 30 chars).

## Slide 10
Advanced Settings
File Split
Split large capture files by size.
Options: 50, 100, 200, 500 MB or 1 GB
When enabled, files are named:
{prefix}_sniffer_timestamp_part001.pcap
Time Sync
Auto-syncs router time with PC before first capture.
Manual sync available via the Sync button in the status bar.
Ensures .pcap timestamps match
your PC clock for accurate analysis.
Persistent Configuration
All settings are saved to ~/.wifi_sniffer/config.json and automatically restored on next launch.

## Slide 11
07 Troubleshooting
SSH connection fails
Run "where ssh" to check OpenSSH. Enable via Settings > Apps > Optional Features > OpenSSH Client.
Cannot reach router
Verify PC is on the same network. Ping 192.168.1.1. Check router power and Ethernet/WiFi.
tcpdump not found
SSH into router and run "opkg install tcpdump" to install the packet capture tool.
No capture files downloaded
Check that capture was actually started (status shows CAPTURING). Verify SSH stays connected during capture.
WebSocket not connecting
App falls back to HTTP polling automatically. This is normal in EXE mode. Functionality is not affected.
Wrong interface mapping
Click "Detect" in the status bar to auto-detect interfaces via iwconfig frequency analysis.

## Slide 12
Quick Reference
Item | Value
Web UI URL | http://127.0.0.1:5000
Router SSH | ssh root@192.168.1.1
Download Folder | ~/Downloads/
Config File | ~/.wifi_sniffer/config.json
Start Command | python run_v4.py or v4.exe
Filename Format | {Product}_{SWVer}_{Band}_sniffer_{timestamp}.pcap
Key Operations
Start All Captures -
Top toolbar green button
Stop All & Download -
Top toolbar red button (with confirmation)
Apply Config & Restart WiFi -
Top toolbar gear button
Diagnose Connection -
Click the connection status indicator

## Slide 13
Ready to Capture!
Launch the application, configure your bands, and start capturing.
Questions? Click the connection status dot for built-in diagnostics.
WiFi Sniffer Control Panel v4 | NETGEAR | 2026